## Slide 1: Radiological and Environmental Sciences Laboratory
FY2019 MAPEP WEBINAR
July 30, 2019

## Slide 2: MAPEP – Analytical Performance
Performance Based Testing Program – Not Method Based
  Analytical methods are not prescribed by MAPEP
  Analytical Methods used Must generate acceptable results in three areas – Accuracy, Detection Limit, Statistically Zero
  Analytical procedures are tested on real world sample matrices; not easily soluble matrices that have nothing to do with real samples.
  Stated Detection Limits are evaluated through Sensitivity Tests.
  Ability to report Statistically Zero results when activity is not present.
  Onsite assessments are usually not needed and are of little value once Analytical Performance is established.

## Slide 3: MAPEP – PT Samples
PT Samples contain chemical and radiochemical interferences that test analytical issues routinely encountered on real samples that will affect the accuracy of the results.
MAPEP was specifically designed for this over 25 years ago.
Laboratory Control Samples in a simple matrix should never be used to validate the performance and accuracy of an analytical procedure – No real world problems.
Experimental Results are compared directly to the NIST traceable reference values… RESL is NIST’s reference laboratory.

## Slide 4: MAPEP – Performance Based
MAPEP is Not Method Based – It is Performance Based
  There is a belief, that if you follow a procedure, the results obtained are adequate and acceptable whether or not they are accurate and convey what is actually present in the sample.
  Example: Leaching procedures will leave unknown and undetected activities of Pu, Am, U, Tc and other radionuclides in the sample and the environment.
  This thought process makes inaccurate results acceptable simply because an inadequate procedure was followed and documented.

## Slide 5: U-238 in soil
Shown are 18 Lab data out of 45 reported. Only 10 passed. 27 Labs reported zero….
Adequate Analytical Method Inadequate Method

## Slide 6: Non-MAPEP – Method Based Analysis
    https://www.hanford.gov/files.cfm/HASQARD_Focus_Group_Minutes_-_2019-02-26_(APPROVED).pdf
  “The MAPEP samples are performance-based PT samples…”
  “... stated that elimination of MAPEP as a requirement is beneficial for her laboratory…”
  “The 222S laboratory has to modify their procedures from the way they typically handle Hanford samples.”
  “For example, to prepare MAPEP samples in a manner that provides an acceptable result for the MAPEP requires sample preparation using hydrofluoric acid. That reagent is not used with Hanford samples.”
  “The MAPEP knows what the total concentration of an analyte is in the matrix provided and expects that result regardless of method used.”
  “Therefore, MAPEP is not an appropriate program for determining adequate PT results…”
  This type of unscientific thinking makes inaccurate results acceptable by a few, simply because an inadequate procedure was followed and documented.

## Slide 7: MAPEP Program Status
Test Sessions 39 and 40 were completed in FY2019
    Performance Testing of International Labs Reinstated
    Technical Areas of Interest
    Certificates of Accreditation

## Slide 8: MAPEP Program Status
    Test Session 41 is scheduled to ship in early September
    Five different matrices
      Soil, Water, Vegetation, Air Filter and Special Matrix
      19 radionuclides 20 inorganic analytes
    Ten different studies
      MaS, MaW, RdF, RdV, GrW, GrF, XaW, XrM
      UaW, PuW(w/Np-237)

## Slide 9: MAPEP Program Status
    International Participation
    Test Session 36 stopped
    Test Session 39 reinstated
    Automated International MAPEP Application

## Slide 10: Technical Highlights of MAPEP Series 39 and 40
Specific Areas of Interest
  Gross Alpha/Beta (GrW and GrF)
    Screening Alpha/Beta/Gamma Water
  U-235/238 Mass Spectrometry (UaW)
  Pu-239/240 Mass Spectrometry (PuW)
    Np-237(In Series 41)?
  Ra-226 Water
  Tc-99 Soil
  Special Radiological Matrix

## Slide 11: Uranium Mass Spectrometry

## Slide 12: Plutonium Mass Spectrometry

## Slide 13: MAPEP Water
0.858 Bq/L
0.257 Bq/L
0.442 Bq/L
0.672 Bq/L

## Slide 14: Technetium-99

## Slide 15: Performance Evaluation of Tc-99 in Soil
  TcO4- anion should be a completely water soluble species.
  However…
  It has been found that TcO4- is highly insoluble in soils containing “high” levels of silica and complex silicates.
  Treatment of these soils with HF was necessary to obtain accurate results for Tc.

## Slide 16: MaS38 – Technetium-99

## Slide 17: MAPEP Special Radiological Matrix (XrM)
  Real World Matrices
    Concrete
    Asphalt
    Soil containing aged mixed fission products
    Organic matrix – water soluble
    Eggs
    Milk
    Vienna Sausage
    Nasal Swab

## Slide 18: Special Radiological Matrix XrM
Special Radiological Matrix (XrM) – Real Matrix / Unknown Analytes…
  Non punitive, promotes increased scientific capability and credibility …
  Undisclosed sample matrix and radionuclides.
  Results are only evaluated based on bias from the known.
  Acceptance flags are not assigned to results.
Designed to encourage participants to test full analytical capabilities.
Tell your QA people to chill…. This is about Science

## Slide 19: XrM39 Vienna Sausage

## Slide 20: XrM40 Nasal Swab

## Slide 21: Accreditation of Analytical Performance

## Slide 22: Accreditation of Analytical Performance

## Slide 23: Accreditation of Analytical Performance

## Slide 24: Discussion
Questions/Future Performance Testing Sample Needs/Interest?

## Slide 25: Websites and Contact Information
RESL: http://www.id.energy.gov/resl/
MAPEP: http://www/id.energy.gov/resl/mapep
Anita R. Bhatt, RESL Director: 208-526-1273 bhattar@id.doe.gov
David Sill, Sr. Technical Manager Chemistry: 208-526-8031 sillds@id.doe.gov
Shane Steidley, Radiochemist: 208-526-8249 steidlsd@id.doe.gov