## Slide 1: DOELAP Assessor Training Overview of DOE-STD-1111 & DOE-STD-1095
Idaho Falls, ID
September 2026

## Slide 2: DOE-STD-1111-2018
Program Administration
Accreditation Process
Specific performance testing and site assessment criteria
  DOE-STD-1095 Department of Energy Laboratory Accreditation Program for Personnel Dosimetry Systems
Applies to DOE Headquarters, field elements, and contractors working to the requirements of 10 CFR 835 (DOE-STD-1111-2018, DOE-STD-1095-2025)
Administered by the Office of Environmental Compliance and Radiation Protection (EH-11)
Was revised and nearly issued in January 2025. Currently awaiting new standards process.

## Slide 3: DOE-STD-1111-2018 Program Administration & Responsibilities
DOELAP Administrator (§3.1)
  Responsible for the development of policies, procedures, standards and continued improvement
  Makes the final decisions on accreditations, amendments, technical equivalencies and appeals
  Appoints and removes assessors and OSB members

## Slide 4: DOE-STD-1111-2018 Program Administration & Responsibilities
Senior Technical Manager (§3.2)
  Coordinates the accreditation process
  Manages the performance testing program
  Maintains schedules for receipt of applications, performance testing and on-site assessments
  Ensures continued training of assessors
  Makes recommendations on requests for amendments, technical equivalency, or accreditations to the DOELAP Administrator
  Makes recommendations to the OSB and DOELAP Administrator regarding accreditation applications, performance testing, on-site assessments, technical equivalencies, or other DOELAP issues
  Maintains records that support accreditation of dosimetry and radiobioassay programs

## Slide 5: DOE-STD-1111-2018 Program Administration & Responsibilities
Oversight Board (OSB) (§3.3)
  Appointed by the DOELAP Administrator
  Have extensive knowledge and experience in implementing a DOELAP-accredited external dosimetry program
  Each serve a five-year term
  May serve one or more successive terms
OSB Charter (Appendix B)
  Advise the DOELAP Administrator regarding dosimetry or radiobioassay issues
  Support the DOELAP Administrator to ensure technical quality and consistency of DOELAP technical standards and on-site assessments

## Slide 6: DOE-STD-1111-2018 Program Administration & Responsibilities
Assessors (§3.4)
  Recognized by DOELAP as a technical expert
  Trained by DOELAP to perform assessments
  Conduct on-site assessments
  Maintain assessor status by completing DOELAP-sponsored assessor training and participate in at least one on-site assessment triennially
DOE Field Element Managers (§3.5)
  Ensure programs under their management receive and maintain DOELAP accreditation or
  Receive exception from accreditation in accordance with 10 CFR Part 835
  Not necessarily the Site Manager

## Slide 7: DOE-STD-1111-2018 Program Administration & Responsibilities
Performance Testing Laboratory (§3.6)
  Authorized to conduct performance testing for DOELAP
  ANSI/HPS N13.11-2022, American National Standard for Dosimetry – Personnel Dosimetry Performance – Criteria for Testing
  ANSI/HPS N13.32-2018, Performance Testing for Extremity Dosimeters

## Slide 8: Definitions Common to Both DOE Standards
Shall – used to denote a required action that is to be performed
Should – used to denote an action that is expected to be performed unless documentation is provided validating technical equivalence

## Slide 9: DOE-STD-1111-2018 Application for Accreditation (§4.1)
Completed application shall be routed through the cognizant DOE field element for approval and submitted to the STM. The application shall contain the following:
  The identification of a program manager who authenticates the submitted information and is authorized to commit the organization’s resources to secure and maintain accreditation
  The identification of an individual to be the point of contact for routine DOELAP communications and activities
  The requested categories for which accreditation is sought
  A description of each external dosimetry processing system or radiobioassay program employed including specific instrumentation, apparatus, and protocols used
  The submittal of required program documents
  The submittal of the Quality Assurance Manual and supporting documentation.
Along with the application, programs seeking initial accreditation shall also submit a detailed self-assessment of their program using the applicable DOELAP requirements
Consideration for DOELAP accreditation requires the submission of an application including the documented quality assurance program. Initial applicants shall also submit a program self-assessment (DOE-STD-1095-2025 §3.1)

## Slide 10: DOE-STD-1095-2025 Performance Testing (§3.2)
Proficiency in processing shall be demonstrated for each model and type of dosimeter the program intends to use to demonstrate compliance with 10 CFR 835.402
Radiation categories selected in the application shall be representative of the radiation type and energy encountered at any location where dosimeter will be used
Compares the applicant’s reported measurement values to the dose delivered to the dosimeters
Submit 15 dosimeters for each subcategory selected in the application for evaluation, except for the whole body dosimeter subcategories of category II, which require 21 dosimeters
Delivered doses note revealed until after the results for all three rounds of irradiations are reported

## Slide 11: DOE-STD-1095-2025 Performance Testing (§3.2) continued
Minimum of 13 dosimeter results shall be reported for each subcategory, except for whole body dosimeter subcategories of category II, which requires a minimum of 18 dosimeter results to be reported
Applicant shall review the performance testing data for potential improvements
Processing of performance testing dosimeters shall be defined and consistent with routine processing procedures
The same dosimeter, model, type and sensitive element used to assess occupational exposures shall be used during performance testing
Applicants are allowed a maximum of two retests, irrespective of which performance testing category failed

## Slide 12: DOE-STD-1111-2018 On-Site Assessment (§4.3)
Program shall undergo an on-site assessment by DOELAP assessors
For initial accreditation, on-site assessment is conducted after performance testing is completed
Monitoring visit may be conducted after implementation of the new system
Monitoring visit may be conducted if major deficiencies were identified
Following initial accreditation, a triennial assessment is required
Assessors use a checklist provided by DOELAP
Checklists include the requirements of DOE-STD-1095-2025, as well as other referenced consensus standards

## Slide 13: DOE-STD-1111-2018 On-Site Assessment (§4.3) continued
Assessor Selection
  STM assigns minimum of two DOELAP qualified assessors
  STM notifies the applicant program and the cognizant field element of the assessment
Document Review
  STM shall provide assessors with the application, documented quality assurance program, and supporting documentation
  Assessors shall review all aspects of the programs management system
  Assessors may request additional documentation from the program
  In cases where the assessor in coordination with the STM determines that the management system documentation requires significant revision, DOELAP may require the laboratory to improve its documentation and submit it for further review prior to proceeding with the accreditation process

## Slide 14: DOE-STD-1111-2018 On-Site Assessment (§4.4)
Assessors review program documents and records, observe processes, inspect facilities and equipment, and interview personnel
Assessors also review previous DOELAP assessment findings to ensure the corrective actions have been implemented

## Slide 15: DOE-STD-1111-2018 On-Site Assessment (§4.4) continued
Observation: An observation is either a suggested improvement that a program may incorporate at its own discretion or a noteworthy practice. The suggestion is offered to help “fine tune” a program. No written response is required
Deficiency: A deficiency finding has a significant, immediate, and continuing adverse impact on the quality of the dosimetry or radiobioassay program
Concern: A Concern is an element of a program that is considered marginal with respect to compliance with DOELAP criteria, but does not have a significant, immediate, and continuing adverse impact on dosimetry program quality
Complete all corrective actions within one year of the assessment close out meeting. For any corrective action lasting longer than one year, the program shall notify the STM and the appropriate DOE field element. The program shall provide a written justification for why the corrective actions were not completed within one year. The STM may ask for additional documentation, such as a tentative schedule and estimated completion date

## Slide 16: DOE-STD-1111-2018 Corrective Action Plan (§4.5)
Program shall submit a corrective action plan through the cognizant field element to the STM for approval
Corrective action plan shall include the actions to be taken to address the concerns and deficiencies as well as the dates of completion of the actions
Any subsequent modifications to the plan shall be approved by the STM and include evidence that the cognizant field element has been copied

## Slide 17: DOE-STD-1111-2018 Monitoring Visits (§4.6)
May be done at any time during an accreditation period
Verify reported changes to a facility or operation or to explore the reason(s) for poor performance during performance testing
May be performed for the following reasons
  As a follow up to previous on-site assessment
  A continued evaluation of a newly accredited program
  A follow-up of a poor performance testing session
  To evaluate recent programmatic changes that could significantly impact the quality of a program
  To follow up on a technical equivalence request, or
  At the request of the DOE field element.

## Slide 18: DOE-STD-1111-2018 Partial Accreditation (§5.3)
The Administrator may approve partial accreditation for satisfactory performance in one or more of the testing category subsets identified in the application
If a system did not meet the DOELAP performance testing criteria for a particular accreditation category subset, a retest for the failed measurement is scheduled for the next test session
The accreditation process may continue for other requested categories in which the performance testing criteria were met

## Slide 19: DOE-STD-1111-2018 Modifications to Accredited Program (§5.4)
STM shall be notified whenever changes are made to key personnel, processes, procedures, equipment, facilities, software, or other systems that were listed in the application for accreditation
Routine maintenance, where the processes and quality control is formally documented in the program’s quality assurance manual or supporting documentation, is not considered a program modification
Modifications, deletions, or additions to systems, processes, or equipment that were identified in the application of accreditation; that were reviewed during the onsite assessment; that are outside the scope of the accredited configuration control system; or that may indirectly impact the personnel dosimetry or radiobioassay program’s ability to accurately perform, record, and report results shall be reported to the STM within 45 days prior to the change, if feasible.
  that could affect the quality of the data
Change in contact information for key personnel (application) or organization structure.

## Slide 20: DOE-STD-1111-2018 Notification to the STM (§5.4.1)
Examples of changes that require notification include:
  Changes to the laboratory’s management system
  Significant facility changes
  Changes in key senior staff or organization structure
  Significant change to primary policies
  Significant changes to resources
Notification of modifications may be made via email or by official letter correspondence to the STM, with a copy to the cognizant field element. The STM may require additional information or a demonstration of technical equivalence in order to evaluate the status of the accreditation with respect to the modification or to ensure that the modifications meet DOELAP requirements.

## Slide 21: DOE-STD-1111-2018 Technical Equivalence (§5.4.2)
Modifications to processes, equipment or facilities that are different from the DOELAP accredited configuration and directly impact the program’s ability to accurately perform, record, and report dosimeter and radiobioassay results shall require a demonstration of technical equivalence showing the modifications meet or exceed accredited capabilities and commitments as stated in the DOELAP application or quality assurance documentation. Replacement of identical or addition of similar equipment (like for like) shall not normally meet the criteria of a technical equivalence. Demonstrations of technical equivalence shall be reported in writing to the STM 45 days prior to the proposed implementation date, if feasible. Examples of modifications that require technical equivalence include:
  Replacement of a major equipment component
  Changes to critical software
  Change to a dose calculation algorithm
  Change in the analysis mode
  Technical Major changes to analytical procedures or methods
  Employment of new procedures or methods

## Slide 22: DOE-STD-1111-2018 Technical Equivalence (§5.4.2) continued
It is recommended that the authorized program representative discuss the details of the modification and proposed technical verification plan with the STM prior to performing the testing needed to show technical equivalence. The STM may be able to provide additional guidance to ensure the technical equivalence documentation meets DOELAP requirements.
The program shall submit evidence supporting a conclusion that the modified system will be technically equivalent or superior to the accredited system
Documentation to support technical equivalence shall be routed through the cognizant field element for approval
STM reviews and makes recommendation to the DOELAP Administrator
Administrator makes the final determination and notification
May require additional information or verifications to be performed before before granting technical equivalence

## Slide 23: DOE-STD-1111-2018 Amendment (§5.5)
The STM shall be notified if a change in the type or quality of a radiation field or radiological environment occurs or is anticipated. The notification shall describe how the current accredited system is adequate or request an amendment to the current accreditation. A program may request an amendment to a current accreditation through additional performance testing for an existing system or performance testing of a new or supplemental system.
A change to the scope of an accredited or qualified personnel dosimetry or radiobioassay program shall be authorized by an amendment to the Conditions of Accreditation (or Vendor Qualification, see Section 7.) prior to affecting the change
A demonstration of technical equivalence and performance testing may be required prior to approving an accreditation amendment. The DOELAP APR should discuss the details of proposed modification with the DOELAP STM in advance of requesting an accreditation amendment.

## Slide 24: DOE-STD-1111-2018 Appeals (§5.6)
A Program may petition the DOELAP Administrator to appeal an adverse determination regarding
  accreditation, including revoking all or part of the program’s scope of accreditation,
  denial of technical equivalence, or
  denial of amendment requests
Petition to appeal shall be submitted to the DOELAP Administrator no later than 45 days following the receipt of an adverse determination letter.
The petition should explain the reason(s) for the appeal, including appropriate supporting documentation, and shall be submitted to the cognizant field element before forwarding to the DOELAP Administrator
Petition to appeal will be investigated by the DOELAP Administrator. The Administrator may select a group of qualified experts, who are independent of the program petitioning the appeal, to investigate the appeal and provide recommendations.

## Slide 25: DOE-STD-1111-2018 Accreditations in Good Standing (§5.7)
When the program submits the DOELAP application before the application deadline and participates during their regularly assigned test cycle and on-site assessment
  The program’s current accreditation will remain in good standing until an official decision is made by DOELAP
  This includes accreditations that are past the effective end date of their current accreditation and awaiting a formal decision from DOELAP on the accreditation renewal

## Slide 26: DOE-STD-1111-2018 Correspondence (§6)
Initial submittals of documentation to DOELAP STM and Administrator, such as an application, a request, or a corrective action plan, shall include evidence of approval by the cognizant field element representative.
Subsequent submittals to DOELAP shall include evidence that the cognizant DOE field element has been copied

## Slide 27: DOE-STD-1111-2018 Vendor Qualification (§7.1)
Process by which a commercial vendor is evaluated to determine if it can provide dosimetry services that meet DOELAP requirements
  Required to submit an application, a self-assessment, undergo performance testing, and pass an on-site assessment
Ensures that vendors can demonstrate to DOELAP accredited programs, or programs seeking DOELAP accreditation that they can meet DOELAP requirements

## Slide 28: DOE-STD-1111-2018 Programs Using Commercial Vendors (§7.2)
When a DOELAP accredited program uses a commercial vendor, the DOELAP accredited program is
  Responsible for ensuring the vendor maintains compliance with all DOELAP requirements
  This includes conducting initial and recurring on-site assessments.
  Also responsible for ensuring appropriate corrective actions are implemented in response to any deficiencies found during an assessment, including on-site assessments conducted by DOELAP
More detail and specific DOELAP requirements is provided in DOE-STD-1095 Appendix B, Guidance For Programs That Use Service Providers